## Slide 1: Localization of Transmitter using TDOA analysis
Supervisor – Prof. Seshan Srirangarajan
By -
Divyansh Kumar and Gopal Saha

## Slide 2
Defence – Tracking Enemy Radars and Drones
UAV Tracking - Detects unauthorized or enemy UAVs by pinpointing their source location
Mobile Terminal Positioning - Provides accurate position for mobile users even in environments where traditional GPS is unreliable
Medical Tracking - Localizing transmitter-equipped medical devices to track patients and belongings
Why Localize Transmitter ?

## Slide 3
What is TDOA ?
TDOA stands for Time difference of Arrival. Its one of the methods to pinpoint transmitter location
Hyperbolic Multilateration : Each pair of Receiver defines a Hyperbola in 2D (hyperboloid in 3D)
For example Lets Take 3 Receivers forming a triangle and 1 transmitter in 2D plane. Coordinates of R1,R2,R3 are (0,0), (a,0), (
Hyperbolas (between receiver pairs):
Here d12,d23,d13 are the differences in distances from the transmitter to the respective receiver pairs.
Tx (x,y):

## Slide 4
These Distances can be found using Receiver Information
In Simulation we have assumed we know the Receiver information and have calculated dij
Time Delay calculated via cross correlation of time signals received
by both receivers (signal processing part!)
Accuracy Depends on how accurately we calculate dij !
Figure Below shows 10-15% Error in calculation of dij

## Slide 5
Objectives!
Learn Basics of RTL-SDRs, Hackrf one, GNU Radio Campanion
Transmitter and Receiver Placement and circuit simulation
Synchronization among receivers
Data Handling and Cross Correlation
TDOA Calculation and Position Estimation via Visualization